## Slide 1: 使用
Has_queue_create()
Agent->QueueCreate()
New AqlQueue
  hsaKmtCreateQueue()
  New queue = allocate_exec_aligned_memory()
    hsaKmtAllocMemory()
      fmm_allocate_host() = fmm_allocate_host_gpu()/fmm_allocate_host_cpu()
    hsaKmtRegisterMemoryToNodes()
    hsaKmtMapMemoryToGPU()

## Slide 2: 使用
__fmm_allocate_device() allocate BO
  aperture_allocate_area  mmap_aperture_allocate_aligned() 在cpu内存上map一段内存，并返回地址。
  fmm_allocate_memory_object
    Ioctrl(AMDKFD_IOC_ALLOC_MEMORY_OF_GPU)
    aperture_allocate_object() 创建分配的显存的vm_obj
hsaKmtRegisterMemory()
  fmm_register_memory()
    fmm_register_user_memory()
      __fmm_allocate_device()
hsaKmtMapMemoryToGPU()
  fmm_map_to_gpu()
    _fmm_map_to_gpu() 或 _fmm_map_to_gpu_uerptr()
      Ioctrl(AMDKFD_IOC_MAP_MEMORY_TO_GPU)

## Slide 3: 内存分配
显存分配
hsa_memory_allocate()
runtime_singleton_->AllocateMemory()
region->Allocate()
alloc_flags = AllocateNoFlags
GPU:
IsLocalMemory = true;
IsSystem = false;
fine_grain = false;
mem_flag.HostAccess = 0;
mem_flag.NonPaged = 1;
mem_flag.NoSubstitute = 1; Mem_flag.CoarseGrain = 1;
mem_flag.executeAccess = 0;
mem_flag.AQLQueueMemory = 0;
AllocateKfdMemory()
hsaKmtAllocMemory()
MakeKfdMemoryResident()
hsaKmtMapMemoryToGPUNodes()
fmm_allocate_device()
aperture allocate area
Ioctl(AMDKFD_IOC_ALLOC_MEMORY_OF_GPU)
create vm object
fmm_map_to_gpu()
Ioctl(AMDKFD_IOC_MAP_MEMORY_TO_GPU)
GPUVM:
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_VRAM;
ioc _flag |= KFD_IOC_ALLOC_MEM_FLAGS_EXECUTABLE;
ioc _flag |= KFD_IOC_ALLOC_MEM_FLAGS_NO_SUBSTITUTE
map offset to drm
user app
map_fd = kfd_fd / drm_fd ?
port = PORT_NONE
flag = MAP_PRIVATE | MAP_FIXED

## Slide 4: 内存分配
ringbuffer分配
AllocRegisteredRingBuffer()
runtime_singleton_->AllocateMemory()
region->Allocate()
alloc_flags = AllocateExecutable
CPU:
NodeId = 0
IsLocalMemory = false;
IsSystem = true;
fine_grain = true;
mem_flag.HostAccess = 1;
mem_flag.NonPaged = 0; Mem_flag.CoarseGrain = 0;
mem_flag.executeAccess = 1;
mem_flag.NoSubstitute = 1;
mem_flag.AQLQueueMemory = 0;
AllocateKfdMemory()
hsaKmtAllocMemory()
MakeKfdMemoryResident()
hsaKmtMapMemoryToGPUNodes()
fmm_allocate_host()
aperture allocate area
Ioctl(AMDKFD_IOC_ALLOC_MEMORY_OF_GPU)
create vm object
fmm_map_to_gpu()
Ioctl(AMDKFD_IOC_MAP_MEMORY_TO_GPU)
GTT:
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_GTT;
ioc _flag |= KFD_IOC_ALLOC_MEM_FLAGS_EXECUTABLE;
ioc _flag |= KFD_IOC_ALLOC_MEM_FLAGS_COHERENT;
map offset to drm
runtime_singleton_->system_allocator()
runtime_singleton_->system_allocator_
fmm_allocate_host_gpu()
map_fd = kfd_fd / drm_fd ?
port = PORT_READ | PORT_WRITE
flag = MAP_SHARED | MAP_FIXED
Notes: 每个queue分配一个ringbuffer

## Slide 5: 内存分配
HARDWARE QUEUE分配
allocate queue
allocate_exec_aligned_memory()
allocate_exec_aligned_memory_gpu()
DeviceLocal = nonPage = false
allocate ctx switch
DeviceLocal = nonPage = false
CPU:
NodeId = 0
DeviceLocal = false;
IsSystem = true;
fine_grain = true;
mem_flag.HostAccess = 1;
mem_flag.NonPaged = 0;
Mem_flag.CoarseGrain = 0;
mem_flag.executeAccess = 1;
mem_flag.NoSubstitute = 1;
mem_flag.AQLQueueMemory = 0;
hsaKmtAllocMemory()
hsaKmtMapMemoryToGPUNodes()
fmm_allocate_host()
aperture allocate area
Ioctl(AMDKFD_IOC_ALLOC_MEMORY_OF_GPU)
create vm object
fmm_map_to_gpu()
Ioctl(AMDKFD_IOC_MAP_MEMORY_TO_GPU)
GTT:
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_GTT;
ioc _flag |= KFD_IOC_ALLOC_MEM_FLAGS_EXECUTABLE;
ioc _flag |= KFD_IOC_ALLOC_MEM_FLAGS_COHERENT;
map offset to drm
fmm_allocate_host_gpu()
hsaKmtCreateQueue()
Notes: 与GPU分配CPU内存相同

## Slide 6: 内存分配
Queue eop分配
allocate eop buffer
allocate_exec_aligned_memory()
allocate_exec_aligned_memory_gpu()
DeviceLocal = nonPage = true
GPU:
NodeId = gpuId;
DeviceLocal = true;
fine_grain = false;
mem_flag.HostAccess = 0;
mem_flag.NonPaged = 1;
mem_flag.NoSubstitute = 1; Mem_flag.CoarseGrain = 1;
mem_flag.executeAccess = 1;
mem_flag.AQLQueueMemory = 0;
hsaKmtAllocMemory()
hsaKmtMapMemoryToGPUNodes()
fmm_allocate_device()
aperture allocate area
Ioctl(AMDKFD_IOC_ALLOC_MEMORY_OF_GPU)
create vm object
fmm_map_to_gpu()
GPUVM:
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_VRAM;
ioc _flag |= KFD_IOC_ALLOC_MEM_FLAGS_EXECUTABLE;
ioc _flag |= KFD_IOC_ALLOC_MEM_FLAGS_NO_SUBSTITUTE
map offset to drm
hsaKmtRegisterMemoryToNodes()
fmm_register_memory()
vm_obj->user_ptr
hsaKmtCreateQueue()
Ioctl(AMDKFD_IOC_MAP_MEMORY_TO_GPU)
_fmm_map_to_gpu_userptr()
_fmm_map_to_gpu()
Notes: 与分配GPU显存相同

## Slide 7: 内存分配
EVENT分配
allocate_exec_aligned_memory()
allocate_exec_aligned_memory_gpu()
NodeId = 0
nonPage = true
DeviceLocal = false
hsaKmtAllocMemory()
hsaKmtMapMemoryToGPUNodes()
fmm_allocate_device()
aperture allocate area
Ioctl(AMDKFD_IOC_ALLOC_MEMORY_OF_GPU)
create vm object
fmm_map_to_gpu()
Ioctl(AMDKFD_IOC_MAP_MEMORY_TO_GPU)
GTT:
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_GTT;
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_EXECUTABLE;
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_NO_SUBSTITUTE
map offset to drm
hsaKmtCreateEvent()
CPU:
NodeId = 0
DeviceLocal = false;
fine_grain = true;
mem_flag.HostAccess = 1;
mem_flag.NonPaged = 1;
Mem_flag.CoarseGrain = 0;
mem_flag.executeAccess = 1;
mem_flag.NoSubstitute = 1;
mem_flag.AQLQueueMemory = 0;
Notes: 与分配GPU显存相同

## Slide 8: 内存分配
DOORBELL MAP
fmm_allocate_doorbell()
aperture allocate area
Ioctl(AMDKFD_IOC_ALLOC_MEMORY_OF_GPU)
create vm object
fmm_map_to_gpu()
Ioctl(AMDKFD_IOC_MAP_MEMORY_TO_GPU)
GPUVM:
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_DOORBELL; ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_WRITABLE;
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_COHERENT;
map offset to drm
hsaKmtCreateQueue()
map_doorbell()
map_doorbell_dgpu()
Notes: 与分配GPU显存相同

## Slide 9: 内存分配
MMIO MAP
map_mmio()
__fmm_allocate_device()
aperture allocate area
Ioctl(AMDKFD_IOC_ALLOC_MEMORY_OF_GPU)
create vm object
fmm_map_to_gpu()
Ioctl(AMDKFD_IOC_MAP_MEMORY_TO_GPU)
MMIO:
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_MMIO_REMAP;
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_WRITABLE;
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_COHERENT;
map offset to drm
Notes: 与分配GPU显存相同

## Slide 10: 内存分配
Allocate device函数
fmm_allocate_device()
__fmm_allocate_device()
aperture_allocate_area()
fmm_allocate_memory_object()
mmap_aperture_allocate_aligned()
aperture allocate area
Ioctl(AMDKFD_IOC_ALLOC_MEMORY_OF_GPU)
create vm object
map offset to drm

## Slide 11: 内存分配
 | 位置 | NodeId | HostAccess | NonPaged
user | GPUVM | GpuId | 0 | 1
Ring buffer | GTT | 0 | 1 | 0
Eop buffer | GPUVM | GpuId | 0 | 1
Doorbell | GPUVM |  |  | 
Kmt_queue | GTT |  | 1 | 0
Context switch | GTT |  | 1 | 0
Event | GTT | 0 | 1 | 1
MMIO | MMIO |  |  | 
总结

## Slide 12
执行队列流程
Init()
InitDispatch()
SetupExecutable()
Setup()
RunDispatch()
hsa_queue_create()
hsa_signal_create()
hsa_queue_add_write_index_relaxed()
hsa_queue_t * queue
hsa_signal_t signal
init aql
packet_index
LoadCodeObjectFromFile()
hsa_code_object_deserialize()
hsa_code_object_t code_object
hsa_executable_create()
hsa_executable_load_code_object()
hsa_executable_freeze()
hsa_executable_get_symbol()
hsa_executable_t executable
Load code_object to executable
Freeze executable
hsa_executable_symbol_t kernel_symbol
Set up aql
aql->kernel_object = code_handle
Fill kernel arg buffer
aql->kernarg_address = kernarg
Set up aql
aql->grid_size_x/y/z; aql->workgroup_size_x/y/z
aql = queue->base_address + packet_index
aql->completion_signal = signal
hsa_signal_store_relaxed()
queue->doorbell_signal
Wait()
hsa_signal_wait_acquire()
signal

## Slide 13: 初始化
hsa_init()
runtime_singleton_->Acquire()
runtime_singleton_->Load()
amd::Load()
LoadExtensions()
amd::hsa::loader::Loader::Create()
new AmdHsaCodeLoader()
AmdHsaCodeLoader::Context * context = Runtime::LoaderContext loader_context_
HSA初始化
Notes: Runtime_singletion 含有一个 loader_
Loader_ 含有多个 excuter, 类型为 Executable
一个executer 含有多个

## Slide 14: 初始化
hsaKmtOpenKFD()
topology_sysfs_get_system_props()
fmm_init_process_apertures()
AmdHsaCodeLoader::Context * context = Runtime::LoaderContext loader_context_
KMT初始化
init_process_doorbells()

## Slide 15: 初始化
amd::Load()
DiscoverGpu()
new GpuAgent()
runtime_singleton_->RegisterAgent()
InitRegionList()
InitCacheList()
BuildTopology()
Ageng初始化

## Slide 16: 初始化
GpuAgent::InitRegionList()
hsaKmtGetNodeMemoryProperties()
填充 HsaMemoryProperties
HeapTypet = HSA_HEAPTYPE_FRAME_BUFFER_PRIVATE
new MemoryRegion()
fine_grain = false
full_profile = false
mem_flag_.NoSubstitute = 1
mem_flag_.HostAccess = 0
mem_flag_. NonPaged = 1
mem_flag_. CoarseCrain = 1
IsLocalMemory() = true
regions_ = region
local_regions_ = region
  填充agent的regions_和local_region_变量
    GPU节点只有一个MemoryBank(region)
    属性为HAS_HEAPTYPE_FRAM_BUFFER_PRIVATE
    判断为 LocalMemory
    填充该region的mem_flag用于alloc()
Ageng memory初始化
Notes: properties_.NumMemoryBanks 是从 “vim /sys/devices/virtual/kfd/kfd/topology/nodes/1/properties” 读取 “mem_banks_count”
properties_. NumMemoryBanks = 1
hsaKmtGetNodeMemoryProperties() 从 “/sys/devices/virtual/kfd/kfd/topology/nodes/1/mem_banks/0/properties” 读取

## Slide 17: 初始化
GpuAgent::InitCacheList()
hsaKmtGetNodeCacheProperties ()
填充 CacheProperties
忽略Instruction属性的cache
  填充agent的caches_变量
    GPU节点有92个Cache
    属性为Instruction将被忽略
    Vega20 有76个cache
      60个L1 cache 大小为16KB
      16个L1 cache 大小为4KB
cache_props_ = cache
Ageng cache初始化
Notes: properties_.NumCaches 是从 “vim /sys/devices/virtual/kfd/kfd/topology/nodes/1/properties” 读取 “caches_count”
properties_.NumCaches = 92
hsaKmtGetNodeMemoryProperties() 从 “/sys/devices/virtual/kfd/kfd/topology/nodes/1/caches/xxx/properties” 读取

## Slide 18: Loader & execute obj
hsa_code_object_deserialize()
amd::hsa::loader::Loader::Create()
loader_ = new AmdHsaCodeLoader()
allocate device(code_obj_size)
memcpy to device(code_obj_size)
find cpu agent and system region
hsa_executable_create_alt()
CreateExecutable()
executables.push new ExecutableImpl()
user app
hsa_executable_create()
create

## Slide 19: Code object
Load elf object, create code object
hsa_executable_load_code_object()
user app
LoadCodeObject()
new AmdHsaCode * code()
code->InitAsHandle()
GElfImage * img
img->initAsBuffer()
pullElf()
get elf header
load segments
load string table
load sections
load symbols
LoadSegments()
LoadSymbol()
ApplyRelocations()
Notes: 1. load code bin file to elf object GElfImage * img
2. load img to code object AmdHsaCode * code
3. create executable from code
address is the code_handle that we use
https://www.man7.org/linux/man-pages/man5/elf.5.html

## Slide 20: Code object
Create executable from code object
hsa_executable_load_code_object()
user app
LoadCodeObject()
new AmdHsaCode * code()
code->InitAsHandle()
GElfImage * img
LoadSegments()
LoadSymbol()
ApplyRelocations()
SegmentAlloc()
LoadSegmentV2()
Memcpy()
address = SymbolAddress()
Memcpy()
Notes: 1. load code bin file to elf object GElfImage * img
2. load img to code object AmdHsaCode * code
3. create executable from code
address is the code_handle that we use
https://www.man7.org/linux/man-pages/man5/elf.5.html

## Slide 21: Code obj & execute obj
core::InterruptSignal::CreateEvent()
signal = new core::InterruptSignal()
queue_inactive_signal = signal
hsa_amd_signal_async_handler()
hsa_executable_create()
hsa_signal_create()
hsa_amd_signal_create()
new core::DefaultSignal()
InterruptSignal::CreateEvent()
hsaKmtCreateEvent()
type = HAS_EVENTTYPE_SIGNAL
manual_reset = false
Notes: sudo apt install libelf-dev
/usr/lib/x86_64-linux-gnu/libelf.a

## Slide 22: Memory copy
blit初始化
InitDma()
blit[] = CreateBlitSdma()
sdma = new BlitSdmaV4()
sdma->Initialize()
hsaKmtCreateQueue()
kQueueSize = 1MB
AllocateExecutable
HSA_QUEUE_SDMA
HwIndexMonotonic = true
SizeToCountOffset = -1
queue_start_addr_ = runtime_singleton_->system_allocator()
signals_[0]/[1] = new InterruptSignal()
GpuAgen->PostToolsInit()
blit[] = CreateBlitKernel ()
Notes: 包括3个blit实例：cpu2gpu, gpu2cpu和gpu2gpu
Blit可以选择sdma也可以选择kernel。而sdma到ram只有两个channel，kernel有32个channel，所以kernel会更快
如果选择sdma, 则每个sdma实例会新建自己的queue,并分配自己的packet buffer。QueueSize = 1MB; QueueType = HAS_QUEUE_SDMA;
如果选择kernel, 则可以为blit指定queue

## Slide 23: Memory copy
Sdma copy
runtime_singleton_->CopyMemory()
gpu_agent->DmaCopy()
SubmitLinearCopyCommand()
BuildCopyCommand()
SubmitBlockingCommand()
SubmitCommand()
ReleaseWriteAddress()
UpdateWriteAndDoorbellRegister()
AcquireWriteAddress()
BuildPollCommand()
BuildHdpFlushCommand()
BuildAtomicDecrementCommand()
hsa_memory_copy()
user app

## Slide 24: signal
初始化
hsa_signal_create()
hsa_amd_signal_create()
hsa_signal = new InterruptSignal()
hsa_signal = new DefaultSignal ()
hsaKmtCreateEvent()
CreateEvent()
hsa_queue_create()
new AqlQueue()
hsa_signal = new InterruptSignal()
hsa_signal = new DefaultSignal ()
queue->completion_signal = signal
HSA_EVENTTYPE_SIGNAL
ManualReset = false
IsSignaled = false
allocate_exec_aligned_memory_gpu()
Ioctl(AMDKFD_IOC_CREATE_EVENT)
Notes: core::g_use_interrupt_wait = 1. use interrupt signal

## Slide 25: signal
operation
hsa_signal_store_relaxed()
StoreRelaxed()
hsa_signal_wait_acquire()
signal.value = value
SetEvent()
hsaKmtSetEvent()
WaitAcquire()
WaitRelaxed()
hsaKmtWaitOnEvent()
Ioctl(AMDKFD_IOC_SET_EVENT)
Ioctl(AMDKFD_IOC_WAIT_EVENTS)
Notes: Default signal don’t use kmt ioctl