## Slide 1: 目录
层次框图
安装与使用
Memory
Sdma
程序对象与执行对象
AQL队列
信号与同步

## Slide 2: 框图
host程序
kernel程序
HIP
OPENCL
HCC
HSA
KMT
AMDKFD
GPU
用户编写的运行在CPU上的程序，包括显存访问，launch kernel 等函数
用户编写的运行在GPU上的程序，包括GPU支持的指令，和运行时定义的函数（如shuffle, atomic 等）
可理解为运行时接口，Hip/ocl只是为了提供不同的语法，方便用户使用开发的warpper
为用户host程序提供接口，包括显存访问，launch kernel，同步等操作。同时还提供编译链调用接口
真正的运行时
基础运行时，为实现”大一统”创建，向上提供CPU/GPU/APU的结点和访存统一，kernel的二进制文件解析，AQL和SDMA/RDMA队列的组包，节点同步等操作的基础API
Thunk layer：内核空间到用户空间的接口，调用驱动层提供的Ioctrl，向上提供统一的内存管理, queue管理等
LLMV
驱动
内核空间
运行时
用户空间
应用程序
用户编写
硬件

## Slide 3: 使用
预安装
  apt-get install libpciaccess-dev
  apt-get install pciutils-dev
下载代码
  git clone https://github.com/RadeonOpenCompute/ROCR-Runtime.git
编译库
  cd ROCR-Runtime/src & mkdir build & cd build
  cmake ../ & make -j16
替换
  sudo cp build/libhsa-runtime64.so* /opt/rocm/lib
链接
  hsa-runtime64
HSa
Notes: sudo apt install libelf-dev
/usr/lib/x86_64-linux-gnu/libelf.a

## Slide 4: 使用
预安装
  apt-get install libpciaccess-dev
  apt-get install pciutils-dev
下载代码
  git clone https://github.com/RadeonOpenCompute/ROCT-Thunk-Interface.git
编译库：
  cd ROCT-Thunk-Interfaces & mkdir build & cd build
  cmake ../ & make -j16
  mkdir lib & cp libhsakmt.so* ../lib
设置kmt库路径：
  export LIBHSAKMT_PATH=/home/feifei/ROCT-Thunk-Interface/
  或者替换：sudo cp build/libkmthsa.so* /opt/rocm/lib
KMT

## Slide 5: 使用
编译测试代码：
  cd .. & cd tests/kfdtest/ & mkdir build &cd build
  cmake & make -j16
运行测试：
  . ./kfdtest --gtest_list_tests
  ./kfdtest --gtest_filter=KFDMemeoryTest.MapMemoryToGPU
KMT gTEST

## Slide 6: 使用
代码位置：/usr/src/amdgpu-version/
编译与安装：
  su
  dkms remove amdgpu/version --all
  dkms install amdgpu/version --force
  reboot
打印：
  dmesg –w&
  dmesg –C: 清空dmesg
驱动状态：dkms status以及lsmod | grep amdgpu
加载驱动：sudo modprobe amdgpu
更新驱动：apt-get remove rocm-dkms & apt-get install rocm-dkms
driver

## Slide 7: 初始化
hsa_init()
runtime_singleton_->Acquire()
runtime_singleton_->Load()
amd::Load()
LoadExtensions()
amd::hsa::loader::Loader::Create()
new AmdHsaCodeLoader()
HSA
  HSA环境由单例core::Runtime::runtime_singleton_维护。管理loader, context, 和agent
  HSA初始化从用户调用has_init() API开始。
    amd::Load(): 负责发现Agent和memory以及Link（这里load是加载的意思）
    amd::hsa::loader::Loader::Create(): 负责创建loader和context（这里loader是code loader）
DiscoverGpu()
BuildTopology()
new GpuAgent()
runtime_singleton_->RegisterAgent()
InitRegionList()
InitCacheList()
创建code loader和context
注册agent
管理agent memory region
Notes: Runtime_singletion 含有一个 loader_
Loader_ 含有多个 excuter, 类型为 Executable
一个executer 含有多个

## Slide 8: 初始化
hsaKmtOpenKFD()
topology_sysfs_get_system_props()
fmm_init_process_apertures()
KMT
init_process_doorbells()
  KMT初始化从HSA调用hsaKmtOpenKFD () API开始。
    打开kfd设备：/dev/kfd
    topology_sysfs_get_system_props()：读取系统属性（节点个数，版本，名称）
      /sys/devices/virtual/kfd/kfd/topology/nodes
      /sys/devices/virtual/kfd/kfd/topology/system_properties
    fmm_init_process_apertures()：获取各节点memory和vm属性（见内存管理）
    init_process_doorbells()：为各节点准备doorbell描述符空间（并不真正分配doorbell）

## Slide 9: 目录
概述
初始化
Allocate
  相关操作
  Allocate device
  Allocate GTT
  Allocate userptr
总结
memory

## Slide 10: memory
概述
显存简单的可以分成三种，
  Remote（GTT）：就是cpu的memory，然后通过gart表映射到gpu让gpu访问。
  Local visible：有pcie的地址，doorbell也分在这里，cpu可以直接访问，map动作只是简单的返回地址。
  Local invisible (Device)：没有pcie地址的，map的时候驱动会分一段cpu memory，操作完unmap再拷贝回去

## Slide 11: memory
概述
USER
DRAM
SP
HVA
HPA
HBM
HPA
SDMA
DPA
BUS_ADDR
DPA
DVA
MMU
GPUVM
IOMMU
GPU
CPU
CP
DVA
GPUVM
BIS_ADDR
Notes: iova->[IOMMU] ->hpa
gpu virtual -> [GPUVM] ->gpu physical
bus address 1.1 (iommu=off) = cpu physical
bus address=GPA 1.2(iommu=on) (iova) ->[IOMMU] ->hpa

## Slide 12: memory
概述
fine-grained memory
  is directly accessible to all the agents in the system at the same time
  Host memory
  System coherence events only at kernel start and end
coarse-grained memory
  may be accessible to multiple agents, but never at the same time
  Device memory
  System coherence happen at the points in the kernel the programmer requests it

## Slide 13: memory
概述
IOMMU(or GART in amd)
  map device dma address to host physical address
  map interruput
无iommu：设备可以通过dma访问全部host地址
有iommu：驱动控制设备dma地址通过iommu映射到某块物理内存

## Slide 14: memory
概述
读取物理内存属性
  在KMT的fmm_init_process_apertures() 中完成，（主要获得heap type属性）
  /sys/devices/virtual/kfd/kfd/topology/nodes/[nodeIdx]/mem_banks/[bankIdx]/properties
  heap_type = 0：HSA_HEAPTYPE_SYSTEM表示CPU系统内存
  heap_type= 2：HSA_HEAPTYPE_FRAME_BUFFER_PRIVATE表示GPU显存

## Slide 15: memory
KMT VM初始化
KMT中VM初始化由fmm_init_process_apertures()完成。KFD是利用DRM的VM
  打开drm设备：/dev/dri/renderD128
  kfd驱动从drm获取vm aperture：KMD aperture
  kmt从kfd获取vm aperture：UMD aperture
  填充gpuvm aperture

## Slide 16: MEMORY
GpuAgent::InitRegionList()
hsaKmtGetNodeMemoryProperties()
填充 HsaMemoryProperties
HeapTypet = HSA_HEAPTYPE_FRAME_BUFFER_PRIVATE
new MemoryRegion()
fine_grain = false
full_profile = false
mem_flag_.NoSubstitute = 1
mem_flag_.HostAccess = 0
mem_flag_. NonPaged = 1
mem_flag_. CoarseCrain = 1
IsLocalMemory() = true
regions_ = region
local_regions_ = region
  填充agent的regions_和local_region_变量
    GPU节点只有一个MemoryBank(region)
    属性为HAS_HEAPTYPE_FRAM_BUFFER_PRIVATE
    判断为 LocalMemory
    填充该region的mem_flag用于alloc()
HSA Ageng memory初始化
Notes: properties_.NumMemoryBanks 是从 “vim /sys/devices/virtual/kfd/kfd/topology/nodes/1/properties” 读取 “mem_banks_count”
properties_. NumMemoryBanks = 1
hsaKmtGetNodeMemoryProperties() 从 “/sys/devices/virtual/kfd/kfd/topology/nodes/1/mem_banks/0/properties” 读取

## Slide 17: MEMORY
GpuAgent::InitCacheList()
hsaKmtGetNodeCacheProperties ()
填充 CacheProperties
忽略Instruction属性的cache
  填充agent的caches_变量
    GPU节点有92个Cache
    属性为Instruction将被忽略
    Vega20 有76个cache
      60个L1 cache 大小为16KB
      16个L1 cache 大小为4KB
cache_props_ = cache
HSA Ageng cache初始化
Notes: properties_.NumCaches 是从 “vim /sys/devices/virtual/kfd/kfd/topology/nodes/1/properties” 读取 “caches_count”
properties_.NumCaches = 92
hsaKmtGetNodeMemoryProperties() 从 “/sys/devices/virtual/kfd/kfd/topology/nodes/1/caches/xxx/properties” 读取

## Slide 18: memory
allocate
CPU
虚拟地址
CPU
物理地址
GPU
虚拟地址
GPU
物理地址
MMU
GPUVM
Drm fd
  包括以下操作：
    在vm aperture上分配空间：匿名mmap，获得addr_user_handle
    让KFD在GPUVM上分配空间：ioctrl
      输入addr_user_handle
      输入user_ptr
      返回buffer_handle
    mmap到drm
    map to GPU：ioctrl
      输入： buffer_handle
Vm_obj
fmm_allocate_device()
__fmm_allocate_device()
aperture_allocate_area()
fmm_allocate_memory_object()
mmap_aperture_allocate_aligned()
aperture allocate area
Ioctl(AMDKFD_IOC_ALLOC_MEMORY_OF_GPU)
create vm object
map offset to drm

## Slide 19: Memory
Allocate device
cpu virtual
mem_size
1. aperture allocated
mem_addr
gpu virtual
mem_size
gpu physical
mem_size
handle
2. IOC_ALLOC_MEMORY_OF_GPU
map_offset
vm_obj.handle
mem_addr
4. IOC_MAP_MEMORY_TO_GPU
vm_obj.handle
User device handle
CPU
GPU
Notes: 1. mem_addr : 进程虚拟地址
2. map_offset: 相对kfd_fd的偏移地址，分配GPUVER
3. map to file : 将进程虚拟地址和文件偏移地址关联
4. 填写GPUVM<->GPUPHY映射表，并传给GPU

## Slide 20: Memory
Allocate device
hsa_memory_allocate()
runtime_singleton_->AllocateMemory()
region->Allocate()
alloc_flags = AllocateNoFlags
GPU:
IsLocalMemory = true;
IsSystem = false;
fine_grain = false;
mem_flag.HostAccess = 0;
mem_flag.NonPaged = 1;
mem_flag.NoSubstitute = 1; Mem_flag.CoarseGrain = 1;
mem_flag.executeAccess = 0;
mem_flag.AQLQueueMemory = 0;
AllocateKfdMemory()
hsaKmtAllocMemory()
MakeKfdMemoryResident()
hsaKmtMapMemoryToGPUNodes()
fmm_allocate_device()
aperture allocate area
Ioctl(AMDKFD_IOC_ALLOC_MEMORY_OF_GPU)
create vm object
fmm_map_to_gpu()
Ioctl(AMDKFD_IOC_MAP_MEMORY_TO_GPU)
GPUVM:
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_VRAM;
ioc _flag |= KFD_IOC_ALLOC_MEM_FLAGS_EXECUTABLE;
ioc _flag |= KFD_IOC_ALLOC_MEM_FLAGS_NO_SUBSTITUTE
map offset to drm
user app
map_fd = kfd_fd / drm_fd ?
port = PORT_NONE
flag = MAP_PRIVATE | MAP_FIXED

## Slide 21: Memory
Allocate gtt
cpu virtual
ringbuffer_size
1. aperture allocated
KFD
ringbuffer_size
mem_addr
gpu virtual
ringbuffer_size
gpu physical
ringbuffer_size
handle
2. IOC_ALLOC_MEMORY_OF_GPU
map_offset
vm_obj.handle
mem_addr
3. mmap
mem_addr
map_offset
4. IOC_MAP_MEMORY_TO_GPU
vm_obj.handle
User ringbuffer_address
CPU
GPU
Notes: 第三步mmap()是把kfd_fd文件，偏移map_offset处， mmio_size大小的内容，映射到mem_addr内存地址。

## Slide 22: 内存分配
HARDWARE QUEUE MALLOC
allocate queue
allocate_exec_aligned_memory()
allocate_exec_aligned_memory_gpu()
DeviceLocal = nonPage = false
allocate ctx switch
DeviceLocal = nonPage = false
CPU:
NodeId = 0
DeviceLocal = false;
IsSystem = true;
fine_grain = true;
mem_flag.HostAccess = 1;
mem_flag.NonPaged = 0;
Mem_flag.CoarseGrain = 0;
mem_flag.executeAccess = 1;
mem_flag.NoSubstitute = 1;
mem_flag.AQLQueueMemory = 0;
hsaKmtAllocMemory()
hsaKmtMapMemoryToGPUNodes()
fmm_allocate_host()
aperture allocate area
Ioctl(AMDKFD_IOC_ALLOC_MEMORY_OF_GPU)
create vm object
fmm_map_to_gpu()
Ioctl(AMDKFD_IOC_MAP_MEMORY_TO_GPU)
GTT:
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_GTT;
ioc _flag |= KFD_IOC_ALLOC_MEM_FLAGS_EXECUTABLE;
ioc _flag |= KFD_IOC_ALLOC_MEM_FLAGS_COHERENT;
map offset to drm
fmm_allocate_host_gpu()
hsaKmtCreateQueue()
Notes: 与GPU分配CPU内存相同

## Slide 23: Memory
 | 位置 | NodeId | HostAccess | NonPaged
user | GPUVM | GpuId | 0 | 1
Ring buffer | GTT | 0 | 1 | 0
Eop buffer | GPUVM | GpuId | 0 | 1
Doorbell | GPUVM |  |  | 
kmt_queue | GTT |  | 1 | 0
Context switch | GTT |  | 1 | 0
Event | GTT | 0 | 1 | 1
MMIO | MMIO |  |  | 
总结

## Slide 24: 内存分配
Ringbuffer malloc
AllocRegisteredRingBuffer()
runtime_singleton_->AllocateMemory()
region->Allocate()
alloc_flags = AllocateExecutable
CPU:
NodeId = 0
IsLocalMemory = false;
IsSystem = true;
fine_grain = true;
mem_flag.HostAccess = 1;
mem_flag.NonPaged = 0; Mem_flag.CoarseGrain = 0;
mem_flag.executeAccess = 1;
mem_flag.NoSubstitute = 1;
mem_flag.AQLQueueMemory = 0;
AllocateKfdMemory()
hsaKmtAllocMemory()
MakeKfdMemoryResident()
hsaKmtMapMemoryToGPUNodes()
fmm_allocate_host()
aperture allocate area
Ioctl(AMDKFD_IOC_ALLOC_MEMORY_OF_GPU)
create vm object
fmm_map_to_gpu()
Ioctl(AMDKFD_IOC_MAP_MEMORY_TO_GPU)
GTT:
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_GTT;
ioc _flag |= KFD_IOC_ALLOC_MEM_FLAGS_EXECUTABLE;
ioc _flag |= KFD_IOC_ALLOC_MEM_FLAGS_COHERENT;
map offset to drm
runtime_singleton_->system_allocator()
runtime_singleton_->system_allocator_
fmm_allocate_host_gpu()
map_fd = kfd_fd / drm_fd ?
port = PORT_READ | PORT_WRITE
flag = MAP_SHARED | MAP_FIXED
Notes: 每个queue分配一个ringbuffer

## Slide 25: Memory allocated
RINGBUFFER malloc
cpu virtual
ringbuffer_size
1. aperture allocated
KFD
ringbuffer_size
mem_addr
gpu virtual
ringbuffer_size
gpu physical
ringbuffer_size
handle
2. IOC_ALLOC_MEMORY_OF_GPU
map_offset
vm_obj.handle
mem_addr
3. mmap
mem_addr
map_offset
4. IOC_MAP_MEMORY_TO_GPU
vm_obj.handle
User ringbuffer_address
CPU
GPU
Notes: 第三步mmap()是把kfd_fd文件，偏移map_offset处， mmio_size大小的内容，映射到mem_addr内存地址。

## Slide 26: 内存分配
HARDWARE QUEUE MALLOC
allocate queue
allocate_exec_aligned_memory()
allocate_exec_aligned_memory_gpu()
DeviceLocal = nonPage = false
allocate ctx switch
DeviceLocal = nonPage = false
CPU:
NodeId = 0
DeviceLocal = false;
IsSystem = true;
fine_grain = true;
mem_flag.HostAccess = 1;
mem_flag.NonPaged = 0;
Mem_flag.CoarseGrain = 0;
mem_flag.executeAccess = 1;
mem_flag.NoSubstitute = 1;
mem_flag.AQLQueueMemory = 0;
hsaKmtAllocMemory()
hsaKmtMapMemoryToGPUNodes()
fmm_allocate_host()
aperture allocate area
Ioctl(AMDKFD_IOC_ALLOC_MEMORY_OF_GPU)
create vm object
fmm_map_to_gpu()
Ioctl(AMDKFD_IOC_MAP_MEMORY_TO_GPU)
GTT:
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_GTT;
ioc _flag |= KFD_IOC_ALLOC_MEM_FLAGS_EXECUTABLE;
ioc _flag |= KFD_IOC_ALLOC_MEM_FLAGS_COHERENT;
map offset to drm
fmm_allocate_host_gpu()
hsaKmtCreateQueue()
Notes: 与GPU分配CPU内存相同

## Slide 27: Memory allocated
Queue eop MALLOC
allocate eop buffer
allocate_exec_aligned_memory()
allocate_exec_aligned_memory_gpu()
DeviceLocal = nonPage = true
GPU:
NodeId = gpuId;
DeviceLocal = true;
fine_grain = false;
mem_flag.HostAccess = 0;
mem_flag.NonPaged = 1;
mem_flag.NoSubstitute = 1; Mem_flag.CoarseGrain = 1;
mem_flag.executeAccess = 1;
mem_flag.AQLQueueMemory = 0;
hsaKmtAllocMemory()
hsaKmtMapMemoryToGPUNodes()
fmm_allocate_device()
aperture allocate area
Ioctl(AMDKFD_IOC_ALLOC_MEMORY_OF_GPU)
create vm object
fmm_map_to_gpu()
GPUVM:
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_VRAM;
ioc _flag |= KFD_IOC_ALLOC_MEM_FLAGS_EXECUTABLE;
ioc _flag |= KFD_IOC_ALLOC_MEM_FLAGS_NO_SUBSTITUTE
map offset to drm
hsaKmtRegisterMemoryToNodes()
fmm_register_memory()
vm_obj->user_ptr
hsaKmtCreateQueue()
Ioctl(AMDKFD_IOC_MAP_MEMORY_TO_GPU)
_fmm_map_to_gpu_userptr()
_fmm_map_to_gpu()
Notes: 与分配GPU显存相同

## Slide 28: Memory allocated
EVENT MALLOC
allocate_exec_aligned_memory()
allocate_exec_aligned_memory_gpu()
NodeId = 0
nonPage = true
DeviceLocal = false
hsaKmtAllocMemory()
hsaKmtMapMemoryToGPUNodes()
fmm_allocate_device()
aperture allocate area
Ioctl(AMDKFD_IOC_ALLOC_MEMORY_OF_GPU)
create vm object
fmm_map_to_gpu()
Ioctl(AMDKFD_IOC_MAP_MEMORY_TO_GPU)
GTT:
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_GTT;
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_EXECUTABLE;
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_NO_SUBSTITUTE
map offset to drm
hsaKmtCreateEvent()
CPU:
NodeId = 0
DeviceLocal = false;
fine_grain = true;
mem_flag.HostAccess = 1;
mem_flag.NonPaged = 1;
Mem_flag.CoarseGrain = 0;
mem_flag.executeAccess = 1;
mem_flag.NoSubstitute = 1;
mem_flag.AQLQueueMemory = 0;
Notes: 与分配GPU显存相同

## Slide 29: Memory allocated
DOORBELL MAP
fmm_allocate_doorbell()
aperture allocate area
Ioctl(AMDKFD_IOC_ALLOC_MEMORY_OF_GPU)
create vm object
fmm_map_to_gpu()
Ioctl(AMDKFD_IOC_MAP_MEMORY_TO_GPU)
GPUVM:
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_DOORBELL; ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_WRITABLE;
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_COHERENT;
map offset to drm
hsaKmtCreateQueue()
map_doorbell()
map_doorbell_dgpu()
Notes: 与分配GPU显存相同

## Slide 30: Memory allocated
Doorbell MAP
cpu virtual
doorbell_size
1. aperture allocated
Kfd_fd
doorbell_size
mem_addr
gpu virtual
doorbell_size
gpu physical
doorbell_size
handle
2. IOC_ALLOC_MEMORY_OF_GPU
map_offset
vm_obj.handle
mem_addr
3. mmap
mem_addr
doorbell_offset
4. IOC_MAP_MEMORY_TO_GPU
vm_obj.handle
User doorbell_address
CPU
GPU
doorbell_offset
Notes: doorbell_offset from IOC_CREATE_QUEUE
doorbell_addr = mem_addr

## Slide 31: Memory allocated
MMIO MAP
map_mmio()
__fmm_allocate_device()
aperture allocate area
Ioctl(AMDKFD_IOC_ALLOC_MEMORY_OF_GPU)
create vm object
fmm_map_to_gpu()
Ioctl(AMDKFD_IOC_MAP_MEMORY_TO_GPU)
MMIO:
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_MMIO_REMAP;
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_WRITABLE;
ioc_flag |= KFD_IOC_ALLOC_MEM_FLAGS_COHERENT;
map offset to drm
Notes: 与分配GPU显存相同

## Slide 32: Memory allocated
MMIO MAP
cpu virtual
page_size
1. aperture allocated
KFD_FD
page_size
mem_addr
gpu virtual
page_size
gpu physical
page_size
handle
2. IOC_ALLOC_MEMORY_OF_GPU
map_offset
vm_obj.handle
mem_addr
3. mmap
mem_addr
map_offset
4. IOC_MAP_MEMORY_TO_GPU
vm_obj.handle
User mmio_address
CPU
GPU
Notes: Mmio_size = page_size

## Slide 33: 目录
概述
初始化
HAS SDMA COPY
SDMA QUEUE
SDMA PACKET
HSA kernel COPY
sdma

## Slide 34: sdma
num_sdma_engines和num_sdma_queues_per_engine从/sys/devices/virtual/kfd/kfd/topology/nodes/[nodeIdx]/properties中读取
Host到device的拷贝，用SDMA，device到device的拷贝使用kernel
Sdma支持写，拷贝和atomic操作
概述

## Slide 35: SDMA
blit初始化
InitDma()
blit[] = CreateBlitSdma()
sdma = new BlitSdmaV4()
sdma->Initialize()
hsaKmtCreateQueue()
kQueueSize = 1MB
AllocateExecutable
HSA_QUEUE_SDMA
HwIndexMonotonic = true
SizeToCountOffset = -1
queue_start_addr_ = runtime_singleton_->system_allocator()
signals_[0]/[1] = new InterruptSignal()
GpuAgen->PostToolsInit()
blit[] = CreateBlitKernel ()
Notes: 包括3个blit实例：cpu2gpu, gpu2cpu和gpu2gpu
Blit可以选择sdma也可以选择kernel。而sdma到ram只有两个channel，kernel有32个channel，所以kernel会更快
如果选择sdma, 则每个sdma实例会新建自己的queue,并分配自己的packet buffer。QueueSize = 1MB; QueueType = HAS_QUEUE_SDMA;
如果选择kernel, 则可以为blit指定queue

## Slide 36: SDMA copy
Sdma copy
runtime_singleton_->CopyMemory()
gpu_agent->DmaCopy()
SubmitLinearCopyCommand()
BuildCopyCommand()
SubmitBlockingCommand()
SubmitCommand()
ReleaseWriteAddress()
UpdateWriteAndDoorbellRegister()
AcquireWriteAddress()
BuildPollCommand()
BuildHdpFlushCommand()
BuildAtomicDecrementCommand()
hsa_memory_copy()
user app

## Slide 37: SDMA
Sdma queue
Sdma queue不需要分配eop, ctx_switch_buffer
Sdma queue type = KFD_IOC_QUEUE_TYPE_SDMA
Ringbuffer size 可以分配1MB，随意设置

## Slide 38: SDMA
Sdma packet格式
DW0: HEARDER
  op(dw[7:0]): 1=SDMA_OP_COPY; 2=SDMA_OP_WRITE
  subop(dw[15:8]): 0=LINEAR
DW1: COUNT
  byte_to_copy(dw1[21:0])
DW2: PARAMETER
  Dst_swap(dw[17:16])
  Src_swap(dw[25:24])
DW3: SRC_ADDR_LO
DW4: SRC_ADDR_HI
DW6: DST_ADDR_LO
DW7: DST_ADDR_HI
Dword 0
Dword 6

## Slide 39: Memory copy
Copy kernel
If ((src & 0x3) == (dst & 0x3)) use aligned copy
Kernel name = “CopyAligned”
  Global size = CU_num * 64 * 4
  Group size = 64
4 copy phase:
  1st phase : copy from addr to 256 Byte aligned
  2nd phase: dwordx4 copy till last whole block fit, unroll = 4
    Every thread load 4 dword
    Every group copy 64 * 4(instr_width) * unroll dword
    Every iteration load global_size * 4(instr_width) * unroll dwords
  3rd phase: dword copy till last whole block fit, dword aligend
  4th phase: byte copy till end

## Slide 40: Memory copy
Copy kernel
Copy src addr = 0x0001 ~ 0x10C2
Unroll = 1
Block copy aligne = 64 * 4 = 256 byte
dword aligned end
Block copy aligne end
Block copy aligne start
copy size per block

## Slide 41: 目录

## Slide 42: signal
初始化
hsa_signal_create()
hsa_amd_signal_create()
hsa_signal = new InterruptSignal()
hsa_signal = new DefaultSignal ()
hsaKmtCreateEvent()
CreateEvent()
hsa_queue_create()
new AqlQueue()
hsa_signal = new InterruptSignal()
hsa_signal = new DefaultSignal ()
queue->completion_signal = signal
HSA_EVENTTYPE_SIGNAL
ManualReset = false
IsSignaled = false
allocate_exec_aligned_memory_gpu()
Ioctl(AMDKFD_IOC_CREATE_EVENT)
Notes: core::g_use_interrupt_wait = 1. use interrupt signal

## Slide 43: signal
operation
hsa_signal_store_relaxed()
StoreRelaxed()
hsa_signal_wait_acquire()
signal.value = value
SetEvent()
hsaKmtSetEvent()
WaitAcquire()
WaitRelaxed()
hsaKmtWaitOnEvent()
Ioctl(AMDKFD_IOC_SET_EVENT)
Ioctl(AMDKFD_IOC_WAIT_EVENTS)
Notes: Default signal don’t use kmt ioctl

## Slide 44: 目录

## Slide 45: Code object
Load elf object, create code object
hsa_executable_load_code_object()
user app
LoadCodeObject()
new AmdHsaCode * code()
code->InitAsHandle()
GElfImage * img
img->initAsBuffer()
pullElf()
get elf header
load segments
load string table
load sections
load symbols
LoadSegments()
LoadSymbol()
ApplyRelocations()
Notes: 1. load code bin file to elf object GElfImage * img
2. load img to code object AmdHsaCode * code
3. create executable from code
address is the code_handle that we use
https://www.man7.org/linux/man-pages/man5/elf.5.html

## Slide 46: Code object
Create executable from code object
hsa_executable_load_code_object()
user app
LoadCodeObject()
new AmdHsaCode * code()
code->InitAsHandle()
GElfImage * img
LoadSegments()
LoadSymbol()
ApplyRelocations()
SegmentAlloc()
LoadSegmentV2()
Memcpy()
address = SymbolAddress()
Memcpy()
Notes: 1. load code bin file to elf object GElfImage * img
2. load img to code object AmdHsaCode * code
3. create executable from code
address is the code_handle that we use
https://www.man7.org/linux/man-pages/man5/elf.5.html

## Slide 47: Loader & execute obj
hsa_code_object_deserialize()
amd::hsa::loader::Loader::Create()
loader_ = new AmdHsaCodeLoader()
allocate device(code_obj_size)
memcpy to device(code_obj_size)
find cpu agent and system region
hsa_executable_create_alt()
CreateExecutable()
executables.push new ExecutableImpl()
user app
hsa_executable_create()
create

## Slide 48: Code obj & execute obj
kernel_symbol = hsa_executable_get_symbol(“kernel_name”)
code_handle = hsa_executable_symbol_get_info(kernel_symbol , HSA_EXECUTABLE_SYMBOL_INFO_KERNEL_OBJECT)
user app
aql_queue->kernel_object = code_handle
Notes: kernel_symbol = hsa_executable_get_symbol(“kernel_name”)
code_handle = hsa_executable_symbol_get_info(kernel_symbol, HSA_EXECUTABLE_SYMBOL_INFO_KERNEL_OBJECT)
  code_handle = address
aql_queue->kernel_object = code_handle

## Slide 49
执行队列流程
Init()
InitDispatch()
SetupExecutable()
Setup()
RunDispatch()
hsa_queue_create()
hsa_signal_create()
hsa_queue_add_write_index_relaxed()
hsa_queue_t * queue
hsa_signal_t signal
init aql
packet_index
LoadCodeObjectFromFile()
hsa_code_object_deserialize()
hsa_code_object_t code_object
hsa_executable_create()
hsa_executable_load_code_object()
hsa_executable_freeze()
hsa_executable_get_symbol()
hsa_executable_t executable
Load code_object to executable
Freeze executable
hsa_executable_symbol_t kernel_symbol
Set up aql
aql->kernel_object = code_handle
Fill kernel arg buffer
aql->kernarg_address = kernarg
Set up aql
aql->grid_size_x/y/z; aql->workgroup_size_x/y/z
aql = queue->base_address + packet_index
aql->completion_signal = signal
hsa_signal_store_relaxed()
queue->doorbell_signal
Wait()
hsa_signal_wait_acquire()
signal

## Slide 50: queue
core::InterruptSignal::CreateEvent()
signal = new core::InterruptSignal()
queue_inactive_signal = signal
hsa_amd_signal_async_handler()
hsa_executable_create()
hsa_signal_create()
hsa_amd_signal_create()
new core::DefaultSignal()
InterruptSignal::CreateEvent()
hsaKmtCreateEvent()
type = HAS_EVENTTYPE_SIGNAL
manual_reset = false
Notes: sudo apt install libelf-dev
/usr/lib/x86_64-linux-gnu/libelf.a

## Slide 51: context
用户不可见
在runtime_singleton中的变量，变量名为loader_context_，类型为LoaderContext，继承自Context。用来维护给elf的segment提供访存的函数，实例只在runtime单例中存在

## Slide 52: loader
用户不可见，实例只在runtime单例中存在
在runtime_singleton中的变量，变量名为loader_，类型为AmdHsaCodeLoader，继承自amd::hsa::loader::Loader。
在初始化时由amd::has::loader::Loader::Create()函数创建，讲runtime_singleton中的contex变量传入。
用来管理所有executable对象

## Slide 53: Code_object
用户维护变量，用户可见类型为hsa_code_object_t。内部就是一个指针，与内部的AmdHsaCode类型无关
实际就是编译后二进制文件拷贝到CPU端内存的指针，该内存需要通过KMT分配，GPU可读取。
用户读取二进制文件，赋值给code_object。然后调用hsa_executable_load_code_object()函数，将code_object加载到executable对象。

## Slide 54: Kernel符号
用户维护变量，类型为hsa_executable_symbol_t，即elf的符号类型，内部类型为loader::Symbol。
executable对象通过解析二进制文件获得kernel符号
用户通过hsa_executable_get_symbol()函数从executable中获得kernel符号对象
然后通过hsa_executable_symbol_get_info(HSA_EXECUTABLE_SYMBOL_INFO_KERNEL_OBJECT)函数，获得kernel可执行二进制的地址，最后给到aqlpacket的kernel_object指针

## Slide 55: executable
用户维护变量，用户可见类型为hsa_executable_t，内部类型为ExecutableImpl，继承自Executable。
内部维护
  AmdHsaCode对象。
  ExecutableObject对象的队列objects
  LoadedCodeObjectImpl对象的队列loaded_code_objects
  ProgramSymbolMap类型的program_symbols_，符号map
用户通过hsa_executable_create()函数创建。该函数调用runtime_singleton_.loader_->CreateExecutable()函数。该函数新建Exceutable对象，并压入loader_的executables队列。

## Slide 56: executable
用户调用hsa_executable_load_code_object()函数将code_object对象加载到executable对象。该函数调用executable对象的LoadCodeObject()函数。
  LoadCodeObject()函数接收code_object对象，即二进制程序指针，然后创建AmdHsaCode()对象，也就是自身的code变量。
  创建LoadedCodeObjectImpl对象，并压入objects和loaded_code_objects队列
  LoadSegments()
  LoadSymbol()：加载kernel符号
    新建KernelSymbol符号，加入program_symbols_的map变量
    Kernel符号对象用于后继给aql包赋值
  ApplyRelocations()
加载code_object

## Slide 57: Kernel加载流程
initial
读取二进制文件
创建执行对象
加载CodeObj
获取kernel符号
获取kernel地址